## Slide 1: William Stallings Data and Computer Communications
Chapter 1
Introduction

## Slide 2: A Communications Model
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data

## Slide 3: Simplified Communications Model - Diagram

## Slide 4: Networking
Point to point communication not usually practical
  Devices are too far apart
  Large set of devices would need impractical number of connections
Solution is a communications network

## Slide 5: Circuit Switching
Dedicated communications path established for the duration of the conversation
e.g. telephone network

## Slide 6: Packet Switching
Small chunks (packets) of data at a time
Packets passed from node to node between source and destination
Used for terminal to computer and computer to computer communications
Data sent out of sequence

## Slide 7: Integrated Services Digital Network
ISDN
Designed to replace public telecom system
Wide variety of services
Entirely digital domain

## Slide 8: Asynchronous Transfer Mode
ATM
Evolution of frame relay
Little overhead for error control
Fixed packet (called cell) length
Anything from 10Mbps to Gbps
Constant data rate(Circuit Switching) using packet switching technique

## Slide 9: Local Area Networks
Smaller scope
  Building or small campus
Usually owned by same organization as attached devices
Data rates much higher
Usually broadcast systems
Now some switched systems and ATM are being introduced

## Slide 10: Protocols
Used for communications between entities in a system
Must speak the same language
Entities
  User applications
  e-mail facilities
Systems
  Computer
  Terminal
  Remote sensor

## Slide 11: Key Elements of a Protocol
Syntax
  Data formats
  Signal levels
Semantics
  Control information
  Error handling
Timing
  Speed matching
  Sequencing

## Slide 12: Protocol Architecture
Task of communication broken up into modules
For example file transfer could use three modules
  File transfer application
  Communication service module
  Network access module

## Slide 13: Addressing Requirements
Two levels of addressing required
Each computer needs unique network address
Each application on a (multi-tasking) computer needs a unique address within the computer
  The service access point or SAP

## Slide 14: Protocol Data Units (PDU)
At each layer, protocols are used to communicate
Control information is added to user data at each layer
Transport layer may fragment user data
Each fragment has a transport header added
  Destination SAP
  Sequence number
  Error detection code
This gives a transport protocol data unit

## Slide 15: Operation of a Protocol Architecture

## Slide 16: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
Used by the global Internet
No official model but a working one.
  Application layer
  Host to host(transport layer)
  Internet layer
  Network access layer
  Physical layer

## Slide 17: OSI Model
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers
A theoretical system delivered too late!
TCP/IP is the de facto standard

## Slide 18: OSI Layers, OSI vs TCP/IP
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 19: Standards
Required to allow for interoperability between equipment
Advantages
  Ensures a large market for equipment and software
  Allows products from different vendors to communicate
Disadvantages
  Freeze technology
  May be multiple standards for the same thing

## Slide 20: Standards Organizations
Internet Society
ISO
ITU-T (formally CCITT)
ATM forum