## Slide 1: William Stallings Data and Computer Communications
Chapter 7
Data Link Control

## Slide 2: Flow Control
Ensuring the sending entity does not overwhelm the receiving entity
  Preventing buffer overflow
Transmission time
  Time taken to emit all bits into medium
Propagation time
  Time for a bit to traverse the link

## Slide 3: Stop and Wait
Source transmits frame
Destination receives frame and replies with acknowledgement
Source waits for ACK before sending next frame
Destination can stop flow by not send ACK
Works well for a few large frames

## Slide 4: Stop and Wait Link Utilization

## Slide 5: Fragmentation
Large block of data may be split into small frames
  Limited buffer size
  Errors detected sooner (when whole frame received)
  On error, retransmission of smaller frames is needed
  Prevents one station occupying medium for long periods
Stop and wait becomes inadequate

## Slide 6: Sliding Windows Flow Control
Allow multiple frames to be in transit
Receiver has buffer W long
Transmitter can send up to W frames without ACK
Each frame is numbered
ACK includes number of next frame expected
Sequence number bounded by size of field (k)
  Frames are numbered modulo 2k

## Slide 7: Sliding Window Diagram

## Slide 8: Example Sliding Window

## Slide 9: Error Detection
Additional bits added by transmitter for error detection code
Parity
  Value of parity bit is such that character has even (even parity) or odd (odd parity) number of ones
  Even number of bit errors goes undetected

## Slide 10: Cyclic Redundancy Check
For a block of k bits transmitter generates n bit sequence
Transmit k+n bits which is exactly divisible by some number
Receive divides frame by that number
  If no remainder, assume no error
  For math, see Stallings chapter 7

## Slide 11: Cyclic Redundancy Check
For a block of k bits transmitter generates n bit sequence
Transmit k+n bits which is exactly divisible by some number

## Slide 12: Error Control
Detection and correction of errors
  Lost frames
  Damaged frames
Automatic repeat request
  Error detection
  Positive acknowledgment
  Retransmission after timeout
  Negative acknowledgement and retransmission

## Slide 13: Automatic Repeat Request (ARQ)
Stop and wait
Go back N
Selective reject (selective retransmission)

## Slide 14: Stop and Wait
Source transmits single frame
Wait for ACK
If received frame damaged, discard it
  Transmitter has timeout
  If no ACK within timeout, retransmit
If ACK damaged,transmitter will not recognize it
  Transmitter will retransmit
  Receive gets two copies of frame
  Use ACK0 and ACK1

## Slide 15: Stop and Wait - Pros and Cons
Simple
Inefficient

## Slide 16: Go Back N (1)
Based on sliding window
If no error, ACK as usual with next frame expected
Use window to control number of outstanding frames
If error, reply with rejection
  Discard that frame and all future frames until error frame received correctly
  Transmitter must go back and retransmit that frame and all subsequent frames

## Slide 17: Go Back N - Damaged Frame
Receiver detects error in frame i
  Receiver sends rejection-i
  Transmitter gets rejection-i
  Transmitter retransmits frame i and all subsequent

## Slide 18: Go Back N - Lost Frame (1)
Frame i lost
  Transmitter sends i+1
  Receiver gets frame i+1 out of sequence
  Receiver send reject i
  Transmitter goes back to frame i and retransmits

## Slide 19: Go Back N - Lost Frame (2)
Frame i lost and no additional frame sent
  Receiver gets nothing and returns neither acknowledgement nor rejection
  Transmitter times out and sends acknowledgement frame with P bit set to 1
  Receiver interprets this as command which it acknowledges with the number of the next frame it expects (frame i )
  Transmitter then retransmits frame i

## Slide 20: Go Back N - Diagram

## Slide 21: Selective Reject
Also called selective retransmission
Only rejected frames are retransmitted
Subsequent frames are accepted by the receiver and buffered
Minimizes retransmission
Receiver must maintain large enough buffer
More complex mechanism in transmitter

## Slide 22: Selective Reject - Diagram