## Slide 1: William Stallings Data and Computer Communications
Chapter 10
Packet Switching

## Slide 2: Principles
Circuit switching designed for voice
  Resources dedicated to a particular call
  Much of the time a data connection is idle
  Data rate is fixed
    Both ends must operate at the same rate

## Slide 3: Packet Switching- Basic Operation
Data transmitted in small packets
  Typically 1000 octets
  Longer messages split into series of packets
  Each packet contains a portion of user data plus some control info
Control info
  Routing (addressing) info
Packets are received, stored briefly (buffered) and pass on to the next node
  Store and forward

## Slide 4: Use of Packets

## Slide 5: Advantages
Line efficiency
  Single node to node link can be shared by many packets over time
  Packets queued and transmitted as fast as possible
Data rate conversion
  Each station connects to the local node at its own speed
  Nodes buffer data if required to equalize rates
Packets are accepted even when network is busy
  Delivery may slow down
Priorities can be used

## Slide 6: Switching Technique
Station breaks long message into packets
Packets sent one at a time to the network
Packets handled in two ways
  Datagram
  Virtual circuit

## Slide 7: Datagram
Each packet treated independently
Packets can take any practical route
Packets may arrive out of order
Packets may go missing
Up to receiver to re-order packets and recover from missing packets

## Slide 8: Virtual Circuit
Preplanned route established before any packets sent
Call request and call accept packets establish connection (handshake)
Each packet contains a virtual circuit identifier instead of destination address
No routing decisions required for each packet
Clear request to drop circuit
Not a dedicated path

## Slide 9: Virtual Circuits v Datagram
Virtual circuits
  Network can provide sequencing and error control
  Packets are forwarded more quickly
    No routing decisions to make
  Less reliable
    Loss of a node looses all circuits through that node
Datagram
  No call setup phase
    Better if few packets
  More flexible
    Routing can be used to avoid congested parts of the network

## Slide 10: Packet Size

## Slide 11: Circuit v Packet Switching
Performance
  Propagation delay
  Transmission time
  Node delay

## Slide 12: Routing
Complex, crucial aspect of packet switched networks
Characteristics required
  Correctness
  Simplicity
  Robustness
  Stability
  Fairness
  Optimality
  Efficiency

## Slide 13: Performance Criteria
Used for selection of route
  Minimum hop
  Least cost
  Minimum delay
  Maximum throughput

## Slide 14: Decision Time and Place
Time
  Packet or virtual circuit basis
Place
  Distributed
    Made by each node
  Centralized
  Source

## Slide 15: Network Information Source and Update Timing
Routing decisions usually based on knowledge of network (not always)
Distributed routing
  Nodes use local knowledge
  May collect info from adjacent nodes
  May collect info from all nodes on a potential route
Central routing
  Collect info from all nodes
Update timing
  When is network info held by nodes updated
  Fixed - never updated
  Adaptive - regular updates

## Slide 16: Routing Strategies
Fixed
Flooding
Random
Adaptive

## Slide 17: Fixed Routing
Single permanent route for each source to destination pair
Determine routes using a least cost algorithm
Route fixed, at least until a change in network topology

## Slide 18: Fixed Routing Tables

## Slide 19: Flooding
No network info required
Packet sent by node to every neighbor
Incoming packets retransmitted on every link except incoming link
Eventually a number of copies will arrive at destination
Each packet is uniquely numbered so duplicates can be discarded
Nodes can remember packets already forwarded to keep network load in bounds
Can include a hop count in packets

## Slide 20: Flooding Example

## Slide 21: Properties of Flooding
All possible routes are tried
  Very robust
At least one packet will have taken minimum hop count route
  Can be used to set up virtual circuit
All nodes are visited
  Useful to distribute information (e.g. routing)

## Slide 22: Random Routing
Node selects one outgoing path for retransmission of incoming packet
Selection can be random or round robin
Can select outgoing path based on probability calculation
No network info needed
Route is typically not least cost nor minimum hop

## Slide 23: Adaptive Routing
Used by almost all packet switching networks
Routing decisions change as conditions on the network change
  Failure
  Congestion
Requires info about network
Decisions more complex
Tradeoff between quality of network info and overhead
Reacting too quickly can cause oscillation

## Slide 24: Adaptive Routing - Advantages
Improved performance
Aid congestion control
Complex system
  May not realize theoretical benefits

## Slide 25: Adaptive Routing - Classification
Based on information sources
  Local (isolated)
    Route to outgoing link with shortest queue
    Can include bias for each destination
    Rarely used - do not make use of easily available info
  Adjacent nodes
  All nodes

## Slide 26: Quiz – Not This Week
Quiz – make a client
  Connect to the server( daum.net, port=80)
  Send the message “Test.\n\n” and Print all messages
  Connected to server ...
  Thread start...
  SND 8> Test.
  Server Connection Closed !
  RECV 124> 127 bytes: <!DOCTYPE HTML PUBLIC "-//IETF//DTD HTML 2.0//EN">
  <html><head>
  <title>302 Found</title>
  </head><body>
  <h1>Found</h1>
  <p>The do儆儆?陷즶?j3v|
  RECV 124> 99 bytes: cument has moved <a href="http://status.daum.net/error/error
  403.html">here</a>.</p>
  </body></html>
  dy>
  <h1>Found</h1>
  <p>The do儆儆?陷즶?j3v|